## Slide 1: Modelgeeks Podcast: Painting Cockpits

## Slide 2: Trumpeter 1/32 Mig-21, OOB Cockpit
Agenda:
Painting Cockpits, Step by Step
  Tamiya 1/48 F-4B
Built Cockpit Examples
  Jets and Props
Simple Scratch Build Items
Easy Cockpit Enhancements
Tools, Tips, and Techniques
More Sea Stories…

## Slide 3
Once the base color is sprayed, decide which areas need tape
Use Tamiya Tape
Use a sharp Xacto Knife to cut
Take your time
Don’t have to be exact
Crisp and Clean Lines is the goal
Step 1 (F-4B): Tape the Instruments and Consoles

## Slide 4
Choose the color for the consoles and Instruments
Step 2 (F-4B): Spray the Instruments and Consoles

## Slide 5
Step 3 (F-4B): Drybrush Neutral Gray
Use an older flat and soft brush
Very little paint on the brush
Quick back and forth motion, gradually building up the paint
The gray provides a foundational layer for the switches and details

## Slide 6
Same principle as using Neutral Gray
Use Tamiya XF-2 Flat White
Step 4 (F-4B): Drybrush White

## Slide 7
Step 5 (F-4B): Pick out the Details and Apply a Wash

## Slide 8
Use a Q-Tip to remove the wash
Blend the wash so there are no stark areas
Step 6: Remove the Wash and Blend

## Slide 9
Step 7 (F-4B): Final Detail Painting

## Slide 10
Hasegawa/Paragon 1/32 Mk. XIV
Same process as the F-4:
  Base Coat
  Dry Brush
  Detail Painting and Wash
  Blend the Wash
  Final Detail Painting

## Slide 11
Hasegawa/Paragon 1/32 Mk. XIV: Dry Brush
Base Color mixed with light gray or light tan
Try to avoid lightening with white

## Slide 12
Hasegawa/Paragon 1/32 Mk. XIV: Detail Painting, Wash, and Final Detail Painting

## Slide 13
Hasegawa/Paragon 1/32 Mk. XIV: Detail Painting, Wash, Final Detail Painting

## Slide 14
Trumpeter 1/32 Mig 21 Cockpit, OOB

## Slide 15
Trumpeter 1/32 Mig 21 Cockpit, OOB

## Slide 16
Trumpeter 1/32 Mig 21 Cockpit, OOB

## Slide 17
Monogram Cockpits… OOB
1/48 A-4E

## Slide 18
Tamiya 1/48 A6M3 Type 32 Zero Cockpit by Justin Lentz…
Instrument Panel
Seat and Cockpit

## Slide 19
Tamiya 1/48 F4U-1A Cockpit by Justin Lentz…
*Bondic Pen (Clear Resin) for Instrument Bezel Glass

## Slide 20
1/48 Revell EA-6A Cockpit …OOB

## Slide 21
Hasegawa 1/32 Fw-190 Cockpit…

## Slide 22
Eduard Seatbelts for the Tamiya F-14A

## Slide 23
Simple Scratch-Built Details…
1/48 A-6E Overhead Console
1/48 A-4E Rear Bulkhead

## Slide 24
Simple Scratch-Built Details…
1/48 EA-6A Overhead Console

## Slide 25: Modelgeeks Podcast
Questions??